Daily Report:  Tracking the Plume of Dispersed Oil using Particle Size Distribution Measurements and Fluorescence Intensity Ratios

June 24, 2010

Water samples were collected at four stations for particle size distribution measurements using the LISST-100X particle counter.  A total of 63 LISST samples were analyzed, including duplicates.  Selected samples from depths of elevated fluorescence from the CTD trace were also collected for fluorescence intensity ratio measurements and analyzed using a Quantech Life Sciences fixed wavelength fluorometer.

Figure 1 presents the small droplet (∑ 2.5 - 60µm) particle size data and fluorescence intensity ratios for stations BM103 through BM106.  Station BM103, BM104 and BM105 were 2km, 5km, and 7km west of the wellhead respectively. Station BM106 was 5km south southwest of the wellhead.

The concentration of small particles was low at all depths for stations BM104 and BM106, but were slightly elevated near the surface (<100m) for station BM103. A subsurface plume was detected at stations BM103, BM104 and BM106 by the CTD fluorometer. Only at station BM103 were there elevated small particles.

The fluorescence intensity ratios tended to be similar at the surface to those observed in the previously, except at station BM103 which appeared higher. The ratios associated with the subsurface plume were similar to those seen in previous plumes, with those observed at BM103 being slighter higher then those seen at either BM104 or BM106.

Figure 1: Average small particle concentrations and fluorescence intensity ratios as a function of depth for stations BM103 to BM106.

# Text boxes

IR=3.29

IR=3.30

IR=2.00

Sample ID Coding:

eg.   BM106-01-09-01

Station    Cast#  Depth   Dup#

Sample ID Coding:

eg.  BM105-01-09-01

Station    Cast#  Depth   Dup#

Depth

0.5m

2m

250m

499m

750m

899m

1110m

1454m

Sample

99

11

10

09

08

07

05

01

Intensity Ratio (IR)

Sample ID Coding:

eg. BM103-01-09-01

Station    Cast#  Depth   Dup#

Sample

99

12

11

10

09

07

05

03

01

Depth

0.5m

2m

50m

250m

500m

1099m

1154m

1249m

1479m

Intensity Ratio (IR)

Sample

99

12

11

09

07

05

03

01

Depth

0.5m

3m

500m

1049m

1109m

1159m

1224m

1494m

Intensity Ratio (IR)

Sample ID Coding:

eg.  BM104-01-09-01

Station    Cast#  Depth   Dup#

Intensity Ratio (IR)

Depth

0.5m

2m

81m

225m

600m

1079m

1149m

1199m

1520m

Sample

99

12

11

10

09

07

05

03

01