Daily Report:  Tracking the Plume of Dispersed Oil using Particle Size Distribution Measurements and Fluorescence Intensity Ratios

June 25, 2010

Water samples were collected at four stations for particle size distribution measurements using the LISST-100X particle counter.  A total of 77 LISST samples were analyzed, including duplicates.  Selected samples from depths of elevated fluorescence from the CTD trace were also collected for fluorescence intensity ratio measurements and analyzed using a Quantech Life Sciences fixed wavelength fluorometer.

Figure 1 presents the small droplet (∑ 2.5 - 60µm) particle size data and fluorescence intensity ratios for stations BM107 through BM111.  Station BM107 was 2.7km southwest, BM108 was 2.5km to the south of southwest, BM109 was 1.2km southwest, BM110 was 5km to the southwest, and BM 111 was 3.3km to the northwest of the wellhead.

Elevated concentrations of small particles were observed at depths corresponding to the subsurface plume detected by the CTD fluorometer. The subsurface plume was found at stations BM107, BM108, and BM109, but not at the other two. A slightly higher concentration of small particles was seen at the surface at stations BM 109 and BM111 as compared to the other three.

Generally speaking fluorescence intensity ratios were lower than those recently observed. There appeared to be very little difference in the ratios at the surface versus those at depth, and as well as little variation between stations.

Figure 1: Average small particle concentrations and fluorescence intensity ratios as a function of depth for stations BM107 to BM111.

# Text boxes

Sample          Depth

99                 0.5m

12                  2m

11                250m

10                749m

09                950m

07              1079m

05              1120m

03              1249m

01              1541m

Intensity Ratio (IR)

Sample ID Coding:

eg.  BM109-01-09-01

Station  Cast# DepthDup#

Sample          Depth

99                 0.5m

09                  2m

08                249m

07                899m

05               1149m

01               1405m

Intensity Ratio (IR)                         Sample ID Coding:

eg. BM111-01-09-01

Station   Cast#  Depth Dup#

Sample          Depth

99                 0.5m

12                  2m

11                250m

10                250m

09                500m

08                750m

07              1020m

05              1149m

01              1552m

Intensity Ratio (IR)

Sample ID Coding:

eg. BM110-01-09-01

Station Cast# Depth Dup#

IR=1.81

Sample          Depth

99                 0.5m

12                  2m

11                250m

10                499m

09                950m

07               1100m

05               1153m

03               1199m

01               1566m

Intensity Ratio (IR)

Sample ID Coding:

eg.   BM108-01-09-01

Station   Cast# Depth Dup#

IR=1.65

Sample          Depth

99                 0.5m

12                  2m

11                150m

10                500m

09                939m

07               1130m

05               1159m

03               1199m

01               1538m

Intensity Ratio (IR)

Sample ID Coding:

eg. BM107-01-09-01

Station   Cast#  Depth  Dup#