Daily Report:  Tracking the Plume of Dispersed Oil using Particle Size Distribution Measurements

June 15, 2010

Water samples were collected at five stations for particle size distribution measurements using the LISST-100X particle counter. A total of 82 LISST samples were analyzed, including duplicates. Samples were also collected and stored for shore based fluorescence intensity ratio measurements.

Figure 1 presents the small droplet (∑ 2.5 - 60µm) particle size data for stations OV047 through OV051. LISST analysis and in-situ fluorometry detected a slightly increased small particle concentration in subsurface around 1000m depth in all stations. The LISST compliments the CTD fluorescence signal revealing a slight elevation of small particles at the bottom depths.

Station #			Lat			Long

OV047				28.741417		-88.417597

OV048				28.732010		-88.376790

OV049				28.780754		-88.387846

OV050				28.780347		-88.347809

OV051				28.754515		-88.357993

Figure 1: Average small particle concentrations as a function of depth from stations OV042 to OV046.