Daily Report:  Tracking the Plume of Dispersed Oil using Particle Size Distribution Measurements

June 16, 2010

Water samples were collected at four stations for particle size distribution measurements using the LISST-100X particle counter. A total of 72 LISST samples were analyzed, including duplicates. Samples were also collected and stored for shore based fluorescence intensity ratio measurements.

Figure 1 presents the small droplet (∑ 2.5 - 60µm) particle size data for stations OV052 through OV055. LISST analysis and in-situ fluorometry detected a slightly increased small particle concentration in subsurface around 1000m depth in all stations. The LISST compliments the CTD fluorescence signal revealing a slight elevation of small particles at the depths of 900 to 1000m.

Station #			Lat			Long

OV052				28.754902		-88.291345

OV053				28.779023		-88.305090

OV054				28.798055		-88.330431

OV055				28.806069		-88.365333

Figure 1: Average small particle concentrations as a function of depth from stations OV052 to OV055.