14 July 2010 Ocean Veritas Status Report, Cruise 9 – Day 1

Complied by Dr. Oliver Pelz (BP Sr. Environmental Toxicologist)

1.)	Site Conditions & Sampling Locations

Sunny skies, calm seas with wave height only approximately 1 feet and light winds throughout the day.

The recent cruise data from the Brook McCall revealed a presence of sub-surface oil approximately 3-5 km south-west from the wellhead (report form 7/13/2010). The mission of day 1 of this cruise was to characterize the subsurface oil plume in this area; especially after installations of the new sealing cap.

When at 3 stations no plume (OV106, OV108, and OV109) and a very weak signal at OV107 were detected in this area (in relative close proximity to the wellhead), a station (OV110) in the opposite direction from the wellhead (NW) was selected and tested.

Figure 1 Sampling Stations

3.)	Air Quality

The Industrial Hygienist Doug Childress (CTEH) conducted air monitoring for VOC (4 ( per hr), benzene (1 ( per hr), H2S (2 ( per hr), and SO2 (2 ( per hr) while workers were on deck. His  measurements showed level of VOC, benzene, H2S, and SO2 were found not to be detectable.

4.)	CTD Findings

All equipment functioned properly. A total of 5 CTD casts were completed and results are summarized below in the table and also shown in the above figure. Only the 2nd CTD cast (OV106) had a very weak fluorometric signal at 1200 m.

| Station | Position Description | Fluorescence signal | Signal depth | Comment |
| --- | --- | --- | --- | --- |
| OV106 | 1.5 km SW of the well-head | No plume |  | Odors and fumes were noticed Surface oil sheen was noticed. Patches of weathered burgundy-colored (un-dispersed and dispersed) oil and small weathered globules on surface. The downward cast stopped at 1200 m because of cable problems. This mechanical interruption could have resulted in the observed CTD abnormality reading (due to potential data stalling). This was confirmed by CTD reading upwards when no fluorescence signal increase was measured at 1200 m. Water sample handlers found light oil sheens in sample bottles from surface water (3 & 50m) and above the sea bottom (1150 m, 1175 m, 1210 m). DO minimum ca. 420 m. A second DO decrease at 1170 m was not associated with fluorescence signals |
| OV107 | 4.6 km WSW of the well head | Very Weak | peak at 1175 m | Surface oil sheen was noticed. Water sample handlers found light oil sheens in 1 sample bottle from above the sea bottom at 1175 m). DO minimum around 395 m Slight DO decrease at 1200 m not associated with fluorescence signals. |
| OV108 | 3.3 km SW of the well-head | No Plume |  | Surface oil sheen was noticed. Water sample handlers found light oil sheens at 1175 m) DO decreases at 150 m 250 m, 350m, and 1195 m, and 1310 m were observed and water samples were drawn at these locations in the water column The DO decreases were not associated with any fluorescence signals |
| OV109 | 5.0 km SW of the well-head | No plume |  | Surface oil sheen was noticed. Water sample handlers found light oil sheens in 1 sample bottle at 1150 m DO decreases at 125 m 250 m (double peaks), 450m, and 1100 m, and 1210 m were observed and water samples were drawn at these locations in the water column The DO decreases were not associated with any fluorescence signals |
| OV110 | 3.8 km NE of the well-head | No plume |  | DO minimum around 450 m Water sample handlers found light oil sheens in sample bottles from surface water (3 m) and above the sea bottom (1150 m). |

5.	LISST data

Slightly elevated concentrations of small particles were detected at station OV107, where the in situ CTD fluorometer detected a very weak subsurface plume. Slightly elevated concentrations of small particles were detected at station OV108 where the in situ CTD fluorometer did not detect a subsurface plume; however, there was a change in the dissolved oxygen levels at 1195m. The deep water plume was not evident at Stations OV106, and OV108 through OV110, in either the CTD trace or small particle concentrations. Highly elevated concentrations of small particles were detected at the surface (0.5m) at stations OV106 and OV108. Slightly elevated concentrations of small particles were detected at the surface (0.5m) at stations OV107, OV109 and OV110.

6.	Aquatic Toxicity Testing

6.1	Cruise 8 – Day 8: Results of samples for Rotoxkit M analysis, collected at cruise day 3 of cruise 9 from stations OV101, OV102, and OV103 did not reveal an aquatic toxic adverse effect in any of the samples.

6.2	Cruise 9 – Day 1: Samples for Rotoxkit M analysis were collected from stations OV106, OV 107, and OV110, and results will be available in tomorrow’s report since animals will be incubated for 24-hrs.

7.)	Comparison of dissolved oxygen (DO) concentrations from in situ CTD and a manual probe

All DO concentrations, measured manually with a field probe O2-meter (YSI Ecosense DO 200) were plotted against DO concentrations that are obtained from CTD casts (see addendum). Results of this comparison revealed a satisfying correlation, and therefore support the fact that CDT measurements represent a reliable screening tool to determine oxygen concentrations in the water column

8.) Science Crew

| Name | First Name | Affiliation | Role |
| --- | --- | --- | --- |
| Childress | Doug | CTEH | Industrial Hygienist |
| Mason | Jennifer | DFO | Particle Analysis |
| Kenny | Michelle | DFO | Particle Analysis |
| Pelz | Oliver | BP | Chief Scientist |
| Heinz | Carrie Ann | EM&A | Rotoxkit Technician |
| Freeman | Kyle | Entrix | Water Samples |
| Greenwood | Bill | Entrix | Water Samples |
| Kobeski | Connor | Entrix | Water Samples |
| Bushnell | Mark | Fugro | Party Chief Fugro Team |
| Pallito | Nick | Fugro | Oceanography Team |
| Riggs | Terry | Fugro | Oceanography Team |
| Moore | Brian | Fugro | Navigation |
| Guzzman | Mike | Fugro | Navigation |
| Bekins | Ward | Fugro | Oceanography Team |
| Davis | Joe | EPA | Agency Rep. |
| Marin | Fred | NOAA | Water Profiling |
| Davis | Cab | NOAA | Oceanographer |
| Stogner | Michelle | NOAA | Data Management |
| Jellison | Lucas | NOAA | NDRA |