15 July 2010 Ocean Veritas Status Report, Cruise 9 – Day 2
Complied by Dr. Oliver Pelz (BP Sr. Environmental Toxicologist)

1.	Site Conditions & Sampling Locations

Overcast skies, Mid-morning thunder storms and lightening, seas with wave height approximately 2-4 feet and winds 10 kts. throughout the day.

Day 1 of this cruise revealed no plume at stations OV106, OV108, and OV109 and a very weak signal at OV107 in a 2 - 5 km proximity SW to SSW to the wellhead. No plume was observed at station OV110 in the north-western direction from the wellhead. The mission of day 2 was to find a subsurface oil plume and to subsequently characterize it.

Figure 1 Sampling Stations

3.	Air Quality

The Industrial Hygienist Doug Childress (CTEH) conducted air monitoring for VOC (4  per hr), benzene (1  per hr), H2S (2  per hr), and SO2 (2  per hr) while workers were on deck. His measurements showed level of VOC (between 4.2 ppm – 0.0 ppm), whereas benzene, H2S, and SO2 were found not to be detectable.

4.	CTD Findings

All equipment functioned properly.

At station OV112, the sampling carousel was left at bottom for 50 min because workers were not allowed on deck due to the thunderstorm. During this time the carousel must have struck a sunken object that then caused bending of the frame and three of the Niskin water sampling bottles were either lost or destroyed. Thus, no water samples were collected from this location, but the CTD instruments collected reliable data on the way down (see table).

Today, a total of 6 CTD casts were completed and results are summarized below in the table and also shown in the above figure. Four CTD casts (OV111, OV 112, OV113, and OV114) had a very weak fluorometric signal at approximately 1200 m and for the two casts OV115 and OV116) no plume was identified. It can be assumed that some (environmental) event in the 1200 - 1300 m area is causing the observed slight deflections of the fluorescence and OD signals.

Station	Position / Description	Fluorescence / signal	Signal depth	Comment
OV111	9.9 km W of the well-head	Very Weak	Peak from 1210 - 1225 m, w/ peak maximum at 1223 m	No surface oil sheen was noticed on surface. / DO minimum at ca. 500 m. / Water sample handlers did not find oil sheens in sub-surface sample bottles / Some (environmental) event in the 1200 - 1300 m area is potentially causing the observed slight deflections of the fluorescence and OD signals.
OV112	4.5 km W of the well-head	Very Weak	Peak from 1995 - 1205 m, w/ peak maximum at 1200 m	No surface oil sheen was noticed. / Water sample handlers did not find oil sheens in sub-surface sample bottles / An abnormal CTD reading was noted at 1200 m. The cause of this signal may have been related to potential data stalling due to mechanical interruption and a stop during the cast downward because of cable problems. / DO minimum at ca. 500 m / Some (environmental) event in the 1200 - 1300 m area is potentially causing the observed slight deflections of the fluorescence and OD signals.
OV113	4.8 km WSW of the well-head	Very weak		Surface oil sheen was noticed. / Water sample handlers found light oil sheens in sub-surface sample bottle at 3 m, 50 m, and 1225 m / DO minimum at ca. 500 m / Some (environmental) event in the 1200 - 1300 m area is potentially causing the observed slight deflections of the fluorescence and OD signals.
OV114	6.0 km SW of the well-head	Very weak		Surface oil sheen was noticed. / Water sample handlers found light oil sheens in 1 sub-surface sample bottle at 1200 m / DO minimum at ca. 500 m / Further slight deflections in OD signals were noted in the 1200 - 1300 m area.
OV115	5.0 km SSE of the well-head	No plume		Surface oil sheen was noticed. / Water sample handlers found light oil sheens in sub-surface sample bottle at 3 m, 50 m, and 1135 m / DO minimum around 500 m / Further slight deflections in OD signals were noted in the 1100 - 1200 m area
OV116	3.2 km SSE of the well-head	No plume		This final cast was conducted at the end of the working day to assist in identifying potential target stations for cruise day 3’s sampling activities. No water samples were collected at this station.

5.	LISST data

High particle concentrations were measured at the surface water (0.5 m) of all stations but one. An increase in small particle concentrations was also found in deep sub-surface water of the 1200 - 1300 m area, where the in-situ fluorometer detected only a very weak signal.

6.	Aquatic Toxicity Testing

6.1	Cruise 9 – Day 1: Results of samples for Rotoxkit M analysis, collected from stations OV106, OV 107, and OV110, did not reveal an aquatic toxic adverse effect in any of the samples.

6.2	Cruise 9 – Day 2: Samples for Rotoxkit M analysis were collected from stations OV111, OV113, OV114, and OV115, and results will be available in tomorrow’s report (animals will be incubated for 24-hrs).

7.	Dissolved oxygen (DO) concentrations

7.1	Testing of field probe: an aqueous sodium sulfite solution (5 g/100 ml) was prepared, which by definition does not contain dissolved oxygen. The reading of the O2-meter (YSI Ecosense DO 200) was in deed 0 mg/l. In a second test, sea water was boiled for about 10 min and readings were < 2 mg/l. The results of these experiments show that the used field probe is capable to determine reliable oxygen concentrations in micro-aerobic or anaerobic concentration ranges – if such values would occur.

7.2	Comparison of dissolved oxygen (DO) concentrations from in situ CTD and a manual probe: DO concentrations, measured manually with a field probe O2-meter (YSI Ecosense DO 200) were compared to DO concentrations, obtained from in situ CTD casts (see addendum). Results of this comparison revealed a satisfying correlation, and therefore support the fact that in situ CDT measurements represent a reliable screening tool to determine oxygen concentrations in the water column.

8.) Science Crew

Name	First Name	Affiliation	Role
Childress	Doug	CTEH	Industrial Hygienist
Mason	Jennifer	DFO	Particle Analysis
Kenny	Michelle	DFO	Particle Analysis
Pelz	Oliver	BP	Chief Scientist
Heinz	Carrie Ann	EM&A	Rotoxkit Technician
Freeman	Kyle	Entrix	Water Samples
Greenwood	Bill	Entrix	Water Samples
Kobeski	Connor	Entrix	Water Samples
Bushnell	Mark	Fugro	Party Chief Fugro Team
Pallito	Nick	Fugro	Oceanography Team
Riggs	Terry	Fugro	Oceanography Team
Moore	Brian	Fugro	Navigation
Guzzman	Mike	Fugro	Navigation
Bekins	Ward	Fugro	Oceanography Team
Davis	Joe	EPA	Agency Rep.
Marin	Fred	NOAA	Water Profiling
Davis	Cab	NOAA	Oceanographer
Stogner	Michelle	NOAA	Data Management
Jellison	Lucas	NOAA	NDRA