16 July 2010 Ocean Veritas Status Report, Cruise 9 – Day 3
Complied by Dr. Oliver Pelz (BP Sr. Environmental Toxicologist)

1.	Site Conditions & Sampling Locations

Overcast skies and thunder storm in the morning, sunny skies later in the morning and throughout the day, seas with wave height approximately 4 feet and winds at 10 kts..

Yesterday, a very weak sub-surface plume was observed in the W/ SW direction approximately 3 km from the wellhead. The mission of day 3 was to cover and characterize the S/W further away from the wellhead. The sample storage refrigerators became completely full after sampling at station OV120. Two additional stations (after OV120) were screened with CTD, to assist in identifying potential target stations for other research cruises but no additional water samples were collected.

Figure 1 Sampling Stations

3.	Air Quality

The Industrial Hygienist Doug Childress (CTEH) conducted air monitoring for VOC (4  per hr), benzene (1  per hr), H2S (2  per hr), and SO2 (2  per hr) while workers were on deck. His measurements showed that the levels of VOC, benzene, H2S, and SO2 were found not to be detectable.

4.	CTD Findings

All equipment functioned properly.

The CTD Fluorometer reported a very weak sub-surfaces oil plume peak at stations OV119, and OV122; a weak plume at stations OV117, and OV121; and a moderate plume at station OV120. No plume was detected noted at OV118 (see table below and figure above). The DO measurements revealed that the minimum detected level for DO was 3.85 at station OV118 (very weak plume).

Station	Position / Description	Fluorescence / signal	Signal depth	Comment
OV117	15.4 SW of the well-head	Weak	Peak at 1115 m	No surface oil sheen was noticed on surface. / DO minimum at ca. 450 m. / Water sample handlers did not find oil sheens in sub-surface sample bottles 1150, 1115, 1100, 1005
OV118	20.0 km SW of the well-head	No plume		Surface oil sheen was noticed. / Water sample handlers did not find oil sheens in sub-surface sample bottles / DO minimum at ca. 500 m.
OV119	15.4 km WSW of the well-head	Very weak	Peak at 1115 m	Water sample handlers found light oil sheens in one sub-surface sample bottle at 1090 m / DO minimum at ca. 415 m
OV120	14.2 SSW of the well-head	Moderate	Highest peak at 1125 m	Heavy Surface oil sheen was noticed. / Water sample handlers found light oil sheens in sub-surface sample bottle at 1140, 1125, and 1040 m. / DO minimum at ca. 500 m
OV121	14.7 km S of the well-head	Weak	Highest peak at 850 m	CTD screen only; no water samples were collected (see chapter 1). / DO minimum around 500 m / Further deflections in Fluorescence signal were noted in the 900 - 1000 m area
OV122	10.0 km WSW of the well-head	Very weak	Peak at 1124 m	CTD screen only; no water samples were collected (see chapter 1).

5.	LISST data

High particle concentrations were measured at the surface water (0.5 m) of all stations. Interestingly, the analyses indicated an increase of small particle concentrations at depth where the in-situ fluorometer obtained either a very weak or no signals.

6.	Aquatic Toxicity Testing

6.1	Cruise 9 – Day 2: Results of samples for Rotoxkit M analysis, collected from stations OV111, OV113, and OV114, did not reveal an aquatic toxic adverse effect in any of the samples. Samples from OV115 were not analyzed.

6.2	Cruise 9 – Day 3: Samples for Rotoxkit M analysis were collected from stations OV117, OV119, and OV120, and results will be available in tomorrow’s report (animals will be incubated for 24-hrs).

7.	Comparison of dissolved oxygen (DO) concentrations from in situ CTD and a manual probe
DO concentrations, measured manually with a field probe O2-meter (YSI Ecosense DO 200) were compared to DO concentrations, obtained from the in situ CTD casts (see addendum). Results of this comparison from all days of the cruise (day 1, day 2, and day 3) revealed a correlation of R2 = 0.7085, and therefore supports the fact that in situ CDT measurements represent a acceptable screening tool to determine oxygen concentrations in the water column (see addendum).

8.) Science Crew

Name	First Name	Affiliation	Role
Childress	Doug	CTEH	Industrial Hygienist
Mason	Jennifer	DFO	Particle Analysis
Kenny	Michelle	DFO	Particle Analysis
Pelz	Oliver	BP	Chief Scientist
Heinz	Carrie Ann	EM&A	Rotoxkit Technician
Freeman	Kyle	Entrix	Water Samples
Greenwood	Bill	Entrix	Water Samples
Kobeski	Connor	Entrix	Water Samples
Bushnell	Mark	Fugro	Party Chief Fugro Team
Pallito	Nick	Fugro	Oceanography Team
Riggs	Terry	Fugro	Oceanography Team
Moore	Brian	Fugro	Navigation
Guzzman	Mike	Fugro	Navigation
Bekins	Ward	Fugro	Oceanography Team
Davis	Joe	EPA	Agency Rep.
Marin	Fred	NOAA	Water Profiling
Davis	Cab	NOAA	Oceanographer
Stogner	Michelle	NOAA	Data Management
Jellison	Lucas	NOAA	NDRA