CTD CAST DATA COLLECTION SUMMARY

Vessel on Position
CTD ready for deployment
Call SBE 19 on
Time SBE 19 on
CTD over to 3 meters
Time for CTD in
Start – Pump on
Time for Pump on
Call for 60m/min
Estimated Depth from bridge
Call Estimated Depth –100 to Winch
LISST down
Start LISST
Time LISST start
Altimeter Alarm
Winch Stop at Altimeter Alarm
Bridge Stop at Altimeter Alarm
Screen Capture – Downcast
Right Click Save Picture
Right Click Print to 6500
CTD Depth + Altimeter Correction = Bottom Depth
Real Time Control
Bottle Control
Call Bottle 1 depth to Winch
Call 20 meters to Winch
Call 10 meters to Winch
Call Stop at Bottle 1 depth to Winch
Fire Bottle
Record DO/Bottle Depth/Time
Repeat for all Bottle depths
*Stop – Pump Off*
Time Pump off
Screen Capture - Upcast
Call CTD on board to Winch
SBE 19 off
Time 19 off (CTD on board)
Stop LISST
Time LISST stop
LISST up
Complete Survey Log (Coordinates)
Complete SBE 9 Header File
Scan Survey Log
Down Load SBE 19 data
FileZilla
SBE 9 data
SBE 19 data
LISST Data
ADCP Data
SBE 9 Screen Shots
Site Logs
Daily Reports
Data To NOAA