SBE 9 & 19 Operation

Config files to use for instruments

SBE 9 Con File is same BP CTD Con File 0454.xmlcon
SBE19 (6515) con file: 6516Threevoltages.con
SBE 19 (Backup): 6140 rev 1.con
LISST: factory_zsc_1389

Display Parameters:

Data base

File Convention for data As per BP (NOAA and ROSE do not matter) refer to (Each are on Desktop):

CTD Sampling Data Format and Transmission Specification

Friday, June 04, 2010
Version 1.0
Author: Tim Morgan
Cellphone: 713-408-7120
Email: tim.morgan@bp.com

And

Guidance for Shipboard Data Management Coordinator

Deep Water Integrated Ocean Operations
Deepwater Horizon Oil Spill

Updated May 28, 2010

Prepared by:

EPA Emergency Response DATA Team
NOAA NOS Center for Coastal Monitoring and Assessment (CCMA)
NOAA NOS Integrated Ocean Observing System (IOOS)

Any questions or concerns regarding format changes are to be directed to Andy Brown

Current Convention (May Change)

Folder for NOAA Data Base naming convention

Folder name : 2010_mmdd_OV

    Data file: CTD (SBE9or 19)_OV0xx01_mmddyyyy
        LISST_OV0xx01_mmddyyyy
        LISSTtransect_OV0xx01_mmddyyyy

CTD Header info to be completed with all info prior to being transmitted (including Lat and Lon).

SeasaveV7 Display Parameter

Ensure LISST Time and date are updated when re-installed on pole

CTD setup

ON FGHUIPC 26

SBE9
DO	Channel 0
Flourometer Channel 1
Altimeter Channel 2

ON FGHIPC31

SBE19 6140 (Backup)

SBE9 6515 (BP)