On Station Procedures and Communications
R/V Ocean Veritas Water Quality Monitoring

Preparation
Charge radios nightly, use channel 80A
Conduct radio checks with bridge, lab, back deck, winch
Bridge announces arrival on station

Deploy LISST
Science team prepares to lower LISST
Bridge approves LISST boom deployment
Back deck lowers LISST boom and informs lab and bridge
Lab starts LISST dip data acquisition and informs bridge

Deploy ADCP
Tag lines are tended fore & aft
Winch receives approval from bridge, back deck, and line tenders
ADCP is raised, swung outboard, and lowered to ~ 1 meter
Tag lines are secured to prevent ADCP rotation
Back deck informs lab that ADCP is deployed
Lab begins ADCP data acquisition

Deploy CTD
Science team prepares CTD, informs bridge and back deck when ready
Bridge approves CTD deployment and provides estimated water depth
Back deck starts SBE 19 and informs lab
Port & starboard tag lines are tended
Back deck begins deployment and requests prop wash
SBE 9 is not started until CTD is submerged (no oily surface waters pumped thru SBE 9)
After prop wash, back deck lowers CTD into water
Winch stops at 2 meters, and tells lab CTD at 2 meters depth

Conduct CTD Cast
Lab starts CTD data acquisition and confirms operation
Lab requests winch begin to lower at 60 m/min, informs winch of expected depth
Winch acknowledges and begins lowering
Winch subtracts 100 meters from depth and announces intent to slow at depth -100 meters
Winch reaches depth – 100 meters and slows to 30 meters/min
Lab monitors CTD, watches/listens for altimeter alarm and closely watches depth readout
Upon altimeter alarm, lab tells winch All Stop
Winch stops, lab informs bridge that CTD is at depth, bridge acknowledges
Lab determines bottle trip depths
Lab requests winch raise CTD to bottle trip depth, winch acknowledges/repeats target depth
Lab alerts winch when CTD is 20 meters from target depth, winch acknowledges
Lab alerts winch when CTD is 10 meters from target depth, winch acknowledges
Lab requests winch All Stop at target depth, winch acknowledges
Lab triggers bottle, requests winch raise CTD to next bottle trip depth
Winch acknowledges/repeats target depth
Lab again provides 20 meter, 10 meter, and All Stop requests for remaining bottles

Recover ADCP
Begin ADCP recovery when CTD is at 300 meters depth
Back deck tells lab to stop ADCP data acquisition (instrument damaged by pinging in air)
Tag lines are tended fore & aft
Winch receives approval from bridge, back deck, and line tenders to recover
ADCP is raised, swung inboard, and lowered into shipping crate

Recover CTD
As CTD approaches 2 meters depth, back deck provides eyes looking for CTD
Lab stops CTD at 2 meters depth, back deck provides redundant stop protection for winch
Surface bottle is tripped
Lab stops data acquisition (no oily surface waters pumped thru SBE 9)
Lab tells winch OK to bring CTD on deck
Winch requests/receives permission to bring CTD on deck
A frame is brought inboard and tag lines are snapped onto CTD cable
A frame is sent outboard slightly so that CTD will clear stern
Winch requests a gentle prop wash
Back deck & winch bring CTD aboard
Science team begins to draw water samples

Conduct LISST Transect
Lab shuts down LISST dip data acquisition
Bridge positions ship to begin LISST transect
Bridge tells lab when they’re ready to begin transect
Lab starts LISST transect acquisition and informs bridge to begin transect.
After 10 minutes, lab announces transect complete
Back deck raises LISST boom
Bridge proceeds to next station