# Vessel science party:
Name	Position	Email/Phone
LT Tracy Hamburger	Chief Scientist/ Operations Officer	ops.pisces@noaa.gov / 301-713-7772

# Cruise notes: Completed 10 Deep CTD casts along the 45km arc in clockwise movement from 045 to 180 from wellhead. Survey techs on 12 hour watches. Three physical scientists are helping with 24 hour water sample collection and monitoring EK60 data.
# Daily Operations:
Data Collection	Collected (Y/N)?	Comment
CTD Casts	Y	10 completed
Fluorometry	Y	Sensor on CTD
LISST
Dissolved Oxygen	Y	Sensor on CTD
Sampling – TPH	Y
Sampling – VOA	Y
GCMS	Y
Acoustics	Y	EK 60 on
MOCNESS
PAH Detection
Biota
Rototox
Other:

# Science results and preliminary interpretations: (please attach any figures/images at end of document)
Fluorometry and Dissolved Oxygen preliminary results
StationID	Distance from / Wellhead (km, bearing)	Fluorescence Signal*	Signal Depth (m)	DO Comments
11	45km, 045° T	13.63	1243
12	45 km, 060 ° T	13.52	1169	Around 1150m, DO dropped to 5.5. Observation that sample water temp warmer than normal
13	45km, 075° T	13.84	1476
14	45km, 090° T	14.16	1950
15	45km, 105° T	13.94	1574
16	45 km, 120° T	13.89	2200
17	45 km, 135° T	13.77	2170
18	45 km, 150° T	13.40	1911
19	45 km, 165° T	13.4	1188
20	45 km, 180° T	13.52	1749

*Use Fluorescence Signal scale from Location Table: No Signal (Background); Very Weak (<= 1 mg/m3);
Weak (> 1 mg/m3 and <= 5 mg/m3); Moderate (>5 mg/m3 and <=15 mg/m3); Strong (> 15 mg/m3)

Chemistry: GCMS / HAPSITE

Samples have been analyzed by GCMS with no hits.

Microbial analysis (if applicable)

Other Observations

## Operational / Logistical issues:
## No issues other than data manager sending out the wrong format of ship sample locations. Data manager is working to correct conversion of Lat/ Long positions.
## Planned activities for next 24 hours:

Record EK60 data for seep monitoring. Finish the last 2 southerly 45km stations and move to 60km starting at station bearing 210° T from wellhead until reaching 045 T. Water sample collection at 3 depths per cast unless noticeable low DO reading or fluorescence spike then collect more as necessary. Run samples through GCMS at each station.