Toxicity Testing

Toxicity testing was initiated on 23 May 2010 for water samples collected on the same date. The identifier for each sample collected, along with its corresponding depth can be found in Table 1.

Table 1. Water Samples Collected for Toxicity Testing

| Date | Sample Number | Depth (m) |
| --- | --- | --- |
| 23 May 2010 | 420104-01 | 1250 |
| 23 May 2010 | 420105-01 | 1200 |
| 23 May 2010 | 420106-01 | 1050 |
| 23 May 2010 | 420108-01 | 600 |
| 23 May 2010 | 420112-01 | 0 |
| 24 May 2010 | 460102-01 | 1400 |
| 24 May 2010 | 460103-01 | 1228 |
| 24 May 2010 | 460105-01 | 1100 |
| 24 May 2010 | 460108-01 | 500 |
| 24 May 2010 | 460112-01 | 0 |
| 24 May 2010 | 480103-01 | 1284 |
| 24 May 2010 | 480107-01 | 1100 |
| 24 May 2010 | 480108-01 | 500 |
| 24 May 2010 | 480112-01 | 0 |

Each water sample was serially diluted for toxicity testing into the concentrations found in Table 2.

Table 2. Serial Dilution Concentrations of Water Sample Tested

| Concentration Number | Percent (%) Dilution |
| --- | --- |
| Control | 0 |
| Concentration 5 | 6.25 |
| Concentration 4 | 12.50 |
| Concentration 3 | 25.00 |
| Concentration 2 | 50.00 |
| Concentration 1 | 100.00 |

Rotifers were added to the varying concentrations for each water sample. After a 24-hour incubation period, the number of dead rotifers were tallied. The percent (%) mortality is calculated for each serial dilution. The results from the Rototox M Kit can be found in Table 3. The total mortality number is cumulative over six wells (reps) of 5 rotifers per well. The sample numbers as well as depth of sampling are also listed in Table 3. Due to the low mortality numbers for each toxicant sample tested,

No calculations of LC50s have been possible.

Table 3. Organism Mortality for Toxicant Concentration = 100%

| Sample ID | Depth (m) | # Dead Organisms | % Mortality |
| --- | --- | --- | --- |
| 420104 | 1250 | 4 | 13.33 |
| 420105 | 1200 | 1 | 3.33 |
| 420106 | 1050 | 1 | 3.33 |
| 420108 | 600 |  |  |
| 420112 | 0 |  |  |
| 460102 | 1400 |  |  |
| 460103 | 1228 |  |  |
| 460105 | 1100 |  |  |
| 460108 | 500 |  |  |
| 460112 | 0 |  |  |
| 480103 | 1284 |  |  |
| 480107 | 1100 |  |  |
| 480108 | 500 |  |  |
| 480112 | 0 |  |  |