# Vessel science party:

| Name | Position | Email/Phone |
| --- | --- | --- |
| LT Tracy Hamburger | Chief Scientist/ Operations Officer | ops.pisces@noaa.gov 301-713-7772 |

# Cruise notes:  Departed Pascagoula on August 5th at 1730 to arrive at MC120 at 0600 for personnel transfer with Bigelow.  Transited to 30km south of wellhead and started CTD casts at 0900.  Deep water casts run approximately 2 hours long in depths of 1900m+.  Survey techs on 12 hour watches.  Three physical scientists are helping with 24 hour water sample collection and monitoring EK60 data at sites and between transits to next stations.

# Daily Operations:

| Data Collection | Collected (Y/N)? | Comment |
| --- | --- | --- |
| CTD Casts | Y | 4 completed |
| Fluorometry | Y | Sensor on CTD |
| LISST |  |  |
| Dissolved Oxygen | Y | Sensor on CTD |
| Sampling – TPH | Y |  |
| Sampling – VOA | Y |  |
| GCMS | Y |  |
| Acoustics | Y | EK 60 on |
| MOCNESS |  |  |
| PAH Detection |  |  |
| Biota |  |  |
| Rototox |  |  |
| Other: |  |  |

# Science results and preliminary interpretations:  (please attach any figures/images at end of document)

Fluorometry and Dissolved Oxygen preliminary results

| StationID | Distance from Wellhead (km, bearing) | Fluorescence Signal* | Signal Depth (m) | DO Comments |
| --- | --- | --- | --- | --- |
| 1 | 30km, 180° T | N/A | 1846 | Fluorometer on wrong channel |
| 2 | 30 km, 165 ° T | 12.79 | 1920 |  |
| 3 | 30km, 150° T | 13.28 | 1994 |  |
| 4 | 30 km, 135° T | 14.16 | 1154 |  |

*Use Fluorescence Signal scale from Location Table: No Signal (Background); Very Weak (<= 1 mg/m3);

Weak (> 1 mg/m3 and <= 5 mg/m3); Moderate (>5 mg/m3 and <=15 mg/m3); Strong (> 15 mg/m3)

Chemistry: GCMS / HAPSITE

Samples have been analyzed by GCMS after collection with no hits.

Microbial analysis (if applicable)

Other Observations

## Operational / Logistical issues:

## CTD casts have to run at a slower payout speed during the day, so that the hydro winches don’t overheat.  At night when temps are a little cooler we can run the winches normally.

## Planned activities for next 24 hours:

Record EK60 data.   Continue 30km radius CTD casts until ENE 1200m contour then move out to 45km from wellhead and conduct CTD casts in a clockwise pattern every 15 degrees.